## Slide 3
Inserted unintended strange characters
  When copy text : Teams ▶ ETX
  Found the problem glob libraries
Trap when comment out
  Tcl sees earliest } (closing brace)
Some proc to read & print files
  Learned regular expressions
[Pre Synth] Learned TCL Basics
proc funnyProc {value} {
if {$value} {
return "TRUE"
# } elseif {[puts "COMMENT :)"] == ""} {
# return "COMMENT"
} else {
return "FALSE"
}
return "IT'S IMPOSSIBLE!!!"
}
proc read_list {filename} {
set f [open $filename r]
set tmp_list [split [read $f] "\n"]
set result [regsub -all \{¦\} $tmp_list ""]
return $result
close $filename
}
proc print_file_list { items } {
foreach item $items {
echo [regsub -all ^.*/ $item ""]
}
}

## Slide 4
Did glob wrong libraries
  tcbn12ffcllbwp6t16p96cpdssgnp0p72vm40c_hm_ccs.db
  tcbn12ffcllbwp6t16p96cpdssgnp0p72v125c_hm_ccs.db
  tcbn12ffcllbwp6t16p96cpdssgnp0p72v0c_hm_ccs.db…
Warning (LINK-5)
  Solved by trimming unnecessary libraries
Errors at set_driving_cell / set_load
  Cut out “ULVT”
  : Constraints derived from outside
[Synth] Struggle with Library Settings 1/2
set_driving_cell -lib_cell BUFFD8BWP6T16P96CPDULVT [all_inputs ]
set_load [get_attribute [index_collection [get_lib_pins */BUFFD8BWP6T16P96CPDULVT/I] 0] pin_capacitance] [all_outputs ]
set_driving_cell -lib_cell BUFFD8BWP6T16P96CPD [all_inputs ]
set_load [get_attribute [index_collection [get_lib_pins */BUFFD8BWP6T16P96CPD/I] 0] pin_capacitance] [all_outputs ]

## Slide 5
Warning: The trip points for … (TIM-164)
  Trip Point :
  CCS vs NLDM
[Synth] Struggle with Library Settings 2/2

## Slide 6
[Init_design] Library Settings
$TECH_LIB, $TECH_FILE, $REFERENCE_LIBRARY ??