## Slide 1
Kazuki FURUKAWA
Jun 29, 2022
LeapMind NNP Trial1 - Week1

## Slide 3
Inserted unintended strange characters
  When copy text : Teams ▶ ETX
  Found the problem to glob libraries
Trap when comment out
  Tcl sees earliest } (closing brace)
Some proc to read & print files
  Learned regular expressions
Use return to stop a tcl script
[Pre Synth] Learned TCL Basics
proc funnyProc {value} {
if {$value} {
return "TRUE"
# } elseif {[puts "COMMENT :)"] == ""} {
# return "COMMENT"
} else {
return "FALSE"
}
return "IT'S IMPOSSIBLE!!!"
}
proc read_list {filename} {
set f [open $filename r]
set tmp_list [split [read $f] "\n"]
set result [regsub -all \{¦\} $tmp_list ""]
return $result
close $filename
}
proc print_file_list { items } {
foreach item $items {
echo [regsub -all ^.*/ $item ""]
}
}

## Slide 4
Did glob wrong libraries
  tcbn12ffcllbwp6t16p96cpdssgnp0p72vm40c_hm_ccs.db
  tcbn12ffcllbwp6t16p96cpdssgnp0p72v125c_hm_ccs.db
  tcbn12ffcllbwp6t16p96cpdssgnp0p72v0c_hm_ccs.db…
Warning (LINK-5)
  Solved by trimming unnecessary libraries
Errors at set_driving_cell / set_load
  They are : constraints derived from the outside condition
  Cut off “ULVT”
[Synth] Struggle with Library Settings 1/2
set_driving_cell -lib_cell BUFFD8BWP6T16P96CPDULVT [all_inputs ]
set_load [get_attribute [index_collection [get_lib_pins */BUFFD8BWP6T16P96CPDULVT/I] 0] pin_capacitance] [all_outputs ]
set_driving_cell -lib_cell BUFFD8BWP6T16P96CPD [all_inputs ]
set_load [get_attribute [index_collection [get_lib_pins */BUFFD8BWP6T16P96CPD/I] 0] pin_capacitance] [all_outputs ]

## Slide 5
Warning: The trip points for ... (TIM-164)
What is a Trip Point ?
  Slew between upper & lower voltage threshold
    e.g. 30-70%, 20-80% @ 0.0-0.72V (0-100%)
cf. Timing precision : CCS >> NLDM
  Both CCS & NLDM are .lib files
  In this trial, we should use CCS.
(TIM-164) seems ignorable for this trial.
  Because every libraries define with different trip points.
[Synth] Struggle with Library Settings 2/2

## Slide 6
[Init_design] Library Settings
How treat $TECH_LIB, $TECH_FILE, $REFERENCE_LIBRARY ?
set BASE_DIR /proj/ATEPairChip/RELEASE/Training_Phase1
set LIB_DIR ${BASE_DIR}/Library
set SC_NDM [list ${LIB_DIR}/ndm/tcbn12ffcllbwp6t16p96cpd_c_ccs.ndm]
set MEM_NDM [list ${LIB_DIR}/ndm/sram_macros.ndm]
set REFERENCE_LIBRARY [concat ${LIB_DIR}/ndm_20210611a/tech_only.ndm $SC_NDM $MEM_NDM]
set TECH_FILE ""
set TECH_LIB ${LIB_DIR}/ndm_20210611a/tech_only.ndm

## Slide 7
[Init_design] Result

## Slide 8
[Clock_opt_cts]

## Slide 9
icc2_shell> report_timing -nosplit
****************************************
Report : timing
-path_type full
-delay_type max
-max_paths 1
-report_by design
-nosplit
Design : Bxb
Version: N-2017.09-SP4
Date : Wed Jun 29 17:53:03 2022
****************************************
Information: Timer using 'AWP'. (TIM-050)
Startpoint: idma/storeAdmaQueue/instCountInWord_reg_2_ (rising edge-triggered flip-flop clocked by cloc
k)
Endpoint: idma/storeAdmaQueue/lenMinus1_reg_1_ (rising edge-triggered flip-flop clocked by clock)
Mode: func
Corner: ss72_cworst_CCworst_T_m40c
Scenario: func::ss72_cworst_CCworst_T_m40c
Path Group: clock
Path Type: max
Point Incr Path
--------------------------------------------------------------------------------------------------
clock clock (rise edge) 0.0000 0.0000
clock network delay (ideal) 0.0000 0.0000
idma/storeAdmaQueue/instCountInWord_reg_2_/CP (SDFQD4BWP6T16P96CPD) 0.0000 0.0000 r
idma/storeAdmaQueue/instCountInWord_reg_2_/Q (SDFQD4BWP6T16P96CPD) 0.1005 0.1005 f
idma/storeAdmaQueue/place_opt_SGI80_78484/ZN (NR2D6BWP6T16P96CPD) 0.0206 0.1211 r
idma/storeAdmaQueue/place_opt_SGI81_78485/ZN (INVD4BWP6T16P96CPD) 0.0173 0.1384 f
idma/storeAdmaQueue/place_opt_SGI82_78486/ZN (NR3D8BWP6T16P96CPD) 0.0214 0.1598 r
idma/storeAdmaQueue/alchip32_dc/ZN (INR2D4BWP6T16P96CPD) 0.0403 0.2001 r
idma/storeAdmaQueue/alchip33_dc/ZN (INR2D4BWP6T16P96CPD) 0.0397 0.2398 r
idma/storeAdmaQueue/alchip31_dc/ZN (INR2D4BWP6T16P96CPD) 0.0397 0.2795 r
idma/storeAdmaQueue/alchip53_dc/ZN (INR2D4BWP6T16P96CPD) 0.0395 0.3190 r
idma/storeAdmaQueue/alchip30_dc/ZN (INR2D4BWP6T16P96CPD) 0.0415 0.3605 r
idma/storeAdmaQueue/place_opt_SGI100_78582/ZN (ND2D4BWP6T16P96CPD) 0.0238 0.3843 f
idma/storeAdmaQueue/place_opt_SGI101_78583/ZN (INVD4BWP6T16P96CPD) 0.0156 0.3999 r
idma/storeAdmaQueue/place_opt_SGI100_78537/ZN (ND2D4BWP6T16P96CPD) 0.0185 0.4183 f
idma/storeAdmaQueue/place_opt_SGI101_78538/ZN (INVD4BWP6T16P96CPD) 0.0159 0.4342 r
[Clock_opt_cts]
idma/storeAdmaQueue/place_opt_SGI109_78516/ZN (ND2D6BWP6T16P96CPD) 0.0168 0.4511 f
idma/storeAdmaQueue/place_opt_SGI110_78517/ZN (INVD4BWP6T16P96CPD) 0.0122 0.4633 r
idma/storeAdmaQueue/alchip22_dc/ZN (INR2D4BWP6T16P96CPD) 0.0340 0.4973 r
idma/storeAdmaQueue/alchip3_dc/ZN (INR2D4BWP6T16P96CPD) 0.0403 0.5376 r
idma/storeAdmaQueue/alchip9_dc/ZN (INR2D4BWP6T16P96CPD) 0.0399 0.5775 r
idma/storeAdmaQueue/alchip23_dc/ZN (INR2D4BWP6T16P96CPD) 0.0415 0.6189 r
idma/storeAdmaQueue/alchip24_dc/ZN (INR2D8BWP6T16P96CPD) 0.0416 0.6605 r
idma/storeAdmaQueue/alchip113_dc/ZN (INR2D8BWP6T16P96CPD) 0.0400 0.7006 r
idma/storeAdmaQueue/alchip114_dc/ZN (INR2D4BWP6T16P96CPD) 0.0401 0.7407 r
idma/storeAdmaQueue/alchip139_dc/ZN (INR2D4BWP6T16P96CPD) 0.0422 0.7828 r
idma/storeAdmaQueue/place_opt_SGI89_78496/ZN (INVD4BWP6T16P96CPD) 0.0188 0.8017 f
idma/storeAdmaQueue/place_opt_SGI91_78498/ZN (ND2D4BWP6T16P96CPD) 0.0137 0.8154 r
idma/storeAdmaQueue/place_opt_SGI92_78499/ZN (ND2D8BWP6T16P96CPD) 0.0224 0.8377 f
idma/storeAdmaQueue/alchip276_dc/ZN (INR4D4BWP6T16P96CPD) 0.0273 0.8651 r
idma/storeAdmaQueue/alchip277_dc/ZN (INR4D4BWP6T16P96CPD) 0.0656 0.9307 r
idma/storeAdmaQueue/alchip278_dc/ZN (INR4D4BWP6T16P96CPD) 0.0768 1.0074 r
idma/storeAdmaQueue/alchip15_dc/ZN (INR3D12BWP6T16P96CPD) 0.0703 1.0778 r
idma/storeAdmaQueue/alchip279_dc/Z (MUX2D1BWP6T16P96CPD) 0.0497 1.1275 r
idma/storeAdmaQueue/lenMinus1_reg_1_/D (SDFQD1BWP6T16P96CPD) 0.0001 1.1276 r
data arrival time 1.1276
clock clock (rise edge) 1.2500 1.2500
clock network delay (ideal) 0.0000 1.2500
idma/storeAdmaQueue/lenMinus1_reg_1_/CP (SDFQD1BWP6T16P96CPD) 0.0000 1.2500 r
clock uncertainty -0.1300 1.1200
library setup time -0.0684 1.0516
data required time 1.0516
--------------------------------------------------------------------------------------------------
data required time 1.0516
data arrival time -1.1276
--------------------------------------------------------------------------------------------------
slack (VIOLATED) -0.0761
1